## Slide 1: AUTOMATED WATER LEAKAGE DETECTION AND CONTROL SYSTEM WITH IOT INTEGRATION done by Koushik vishal(RA2211026010384) Kishore Khannan(RA2211026010409) Monesh kumar(RA2211026010415) Divakar(RA2211026010417)

## Slide 2: ABSTRACT:
The water leakage detection and control system is designed to monitor and manage water flow efficiently, preventing wastage and potential damage. It employs two water flow sensors—one at the inlet to measure the total incoming flow and another at the outlet to track the actual flow. Any discrepancy between these readings indicates a leakage in the pipeline. Upon detecting a leakage, the system automatically activates a solenoid valve to shut off the water supply, stopping further wastage. Simultaneously, the pump motor is turned off to halt water flow, ensuring controlled operation. To enhance responsiveness, a GSM module sends an SMS alert to a designated person, notifying them of the leakage incident in real time. Additionally, the system updates the status on an IoT-enabled webpage, allowing remote monitoring and data analysis. This IoT integration provides users with a continuous log of water flow patterns and leakage incidents, enabling proactive maintenance. The system not only conserves water but also reduces operational costs by minimizing damages caused by unnoticed leaks. The real-time monitoring feature ensures that immediate action can be taken upon detecting a fault, enhancing reliability and efficiency. By automating the detection and control process, this project offers a smart and effective solution for residential, industrial, and agricultural water management applications. The combination of flow sensors, solenoid valves, pump motor control, GSM alerts, and IoT integration creates a comprehensive water conservation system that prevents losses, promotes sustainable water usage, and ensures uninterrupted water distribution. The system’s ability to detect, report, and mitigate leakages autonomously makes it a valuable asset in water management infrastructure, providing users with an efficient and cost-effective approach to handling water supply issues. This innovative solution enhances sustainability by preventing excessive water wastage, promoting conservation, and improving overall resource management.

## Slide 3: SCOPE OF THE PROJECT:
The water leakage detection and control system has a wide scope across various sectors where efficient water management is critical. In residential areas, it helps homeowners prevent water wastage and structural damage caused by undetected leaks. In industrial and agricultural settings, where large volumes of water are used, the system ensures minimal resource loss and enhances operational efficiency. The integration of GSM and IoT technologies allows for real-time alerts and remote monitoring, making the system highly effective for smart city applications and modern infrastructure. Additionally, the project contributes to water conservation efforts by detecting leaks early and automating the control process. Its scalable design makes it adaptable for both small and large-scale water distribution networks, positioning it as a vital tool in sustainable resource management and preventive maintenance.

## Slide 4
  EXISTING SYSTEM
Manual Monitoring and Detection – Traditional water leakage detection relies on manual inspection, which is time-consuming, inefficient, and prone to human error, leading to delayed responses and increased water wastage.
Lack of Automated Control – Existing systems do not have an automated mechanism to stop water flow upon detecting a leakage, resulting in continuous wastage and potential damage to infrastructure.
Limited Alert and Monitoring System – Conventional setups lack real-time alerting and remote monitoring via IoT, making it difficult to track leaks instantly and take prompt action to prevent excessive water loss.
EXISTING SYSTEM DISADVANTAGES
Delayed Detection and Response – Manual inspection methods result in slow leak detection, leading to unnecessary water wastage and potential damage before corrective action is taken.
Continuous Water Loss – In the absence of an automated shutoff mechanism, water continues to leak until manually addressed, increasing water bills and resource wastage.
Higher Maintenance Costs – Frequent unnoticed leaks can cause structural damage, requiring costly repairs and replacements in pipelines and water distribution systems

## Slide 5
  PROPOSED SYSTEM
 Automated Leakage Detection and Control – The system uses two water flow sensors to detect discrepancies in water flow, automatically identifying leakages and activating a solenoid valve to shut off the water supply, preventing wastage.
 Real-Time Alerts and IoT Monitoring – A GSM module sends SMS notifications to a designated person upon detecting a leak, while the IoT-enabled webpage updates in real time, allowing remote monitoring and analysis of water flow data.
 Efficient Water Management and Conservation – By integrating automation, real-time alerts, and remote access, the system minimizes water loss, reduces maintenance costs, and ensures sustainable water distribution for residential, industrial, and agricultural applications.
PROPOSED SYSTEM ADVANTAGES
 Automated Leakage Prevention – The system detects leaks in real time and automatically shuts off the water supply, preventing unnecessary water loss and damage.
 Real-Time Alerts and Remote Monitoring – The GSM module sends instant SMS notifications, and IoT integration allows users to monitor the system remotely, ensuring quick response and efficient management.
 Water Conservation and Cost Savings – By stopping leaks immediately, the system helps conserve water, reduces utility bills, and minimizes maintenance costs associated with water damage.

## Slide 6: LITERATURE SURVEY:
Title 1: Smart Water Management Using IOT
Author: Ramratan, Vinayak
Year : 2016
Description:
This paper presents an IOT device which help to manage and plan the usage of water. This system can be easily installed in residential societies. Sensors placed in the tank which continuously informs the water level at the current time. This information will be updated on the cloud and using an android application, user can visualize the water level on a Smartphone anywhere that is connected to Internet. According to the level of water in the tank the motor functioning will be automatically controlled, at low level of water motor will automatically turn on and when tank is about to fill up it will cut off.

## Slide 7
Title 2: An IoT Based Dam Water Management System for Agriculture
Author: Chellaswamy C, Nisha J
Year : 2018
Description:Water plays an important role in our day to day life in various fields. Introduction of new methods to solve the waterrelated problems includes adaptive management, remote sensing with the new concepts such as water security, global integration of information, etc. In this paper, we present an Internet of Things (IoT) based dam water management system (IoT-DWM) for reducing the wastage of water. The proposed IoT-DWM consists of various parts such as field sensing section, IoT network section, and dam control section, etc. The real data can be observed through different sensors placed in the agriculture area and updated it in the cloud. The dam controller receives the real data of the particular area and estimates the water requirement. The water requirement will vary depending upon the crop cultivated in that area. The controller considers different parameters such as types of crop in that area, temperature, humidity, and wind speed while estimating the requirement of water. The simulation result shows that the proposed IoT-DWM provides better results, save water in a considerable amount and leads to reduced water scarcity.

## Slide 8
Title 3: SWAMP: an IoT-based Smart Water Management Platform for Precision Irrigation in Agriculture
Author: Carlos Kamienski1, Juha-Pekka Soininen2
Year : 2020
Description:
Irrigation for agriculture is the biggest consumer of freshwater in the world, which makes a case for the intensive use of technology to optimize the use of water, reduce the consumption of energy and improve the quality of crops. While the Internet of Things (IoT) and other associated technologies are the natural choice for smart water management applications, their appropriateness is still to be proven in real settings with the deployment of on-site pilots. Also, IoT-based application development platforms should be generic enough to be adapted to different crops, climates, and countries. The SWAMP project develops IoT based methods and approaches for smart water management in precision irrigation domain and pilots them in Italy, Spain, and Brazil. In this paper, we present the SWAMP view, architecture, pilots and the scenario-based development process adopted in the project.

## Slide 9
Title 4: Smart Water Management in Housing Societies using IoT
Author: Kaushik Gupta 1 , Mandar Kulkarni
Year : 2018
Description:
In the era of IoT, automation is one of the essential attribute. This increases comfort and convenience in the lives of people. We would like to provide this in the domain of water management. Our motive is to help the readers understand the importance of using water judiciously and equipping them with the knowledge of the functioning of water management system which is done by using Internet of Things (IoT). We also discuss about how this project is the future of sustainable management of water in residences.

## Slide 10
Title 5: IOT Based Water Management System
Author: Vaishnavi Jeurkar
Year : 2020
Description:
Industry utilizes water in different ways. Water being an important commodity is becoming scarce due to droughts and overuse. Industries are not aware of their water consumption and thus water management is complicated for them. This Water Management System is a solution for measuring important industrial water parameters like temperature, water level and water consumption. The system measures all the parameters in real time and can be remotely viewed/controlled over smart phones using Internet of Things (IOT). The system measures water level using a capacitive level sensor. This sensor is based on the principle of change in capacitance due to change in the area of the plates. It overcomes the drawbacks of conventional capacitive level sensor.

## Slide 11
HARDWARE REQUIREMENTS:
1. ARDIUNO UNO
2. WATER FLOW SENSOR
3. IOT
4. MOTOR DRIVER
5. PUMP MOTOR
6. POWE SUPPLY
7. SOLINOID VALVE

## Slide 12: BLOCK DIAGRAM:
ARDIUNO UNO
POWER SUPPLY
WATER FLOW SENSOR(2)
SOLINOID VALVUE
PIPE SETUP
GSM
ANDROID
MOTOR DRIVER
IOT
PUMP MOTOR(2)

## Slide 13: MODULE NAME:
 Water Flow Monitoring Module
 Leakage Control and Prevention Module
 Notification and IoT Monitoring Module

## Slide 14: Water Flow Monitoring Module:
This module is responsible for detecting discrepancies in water flow, indicating possible leakage. It uses two Water Flow Sensors—one installed at the inlet and another at the outlet. These sensors continuously measure the flow rate and send data to the Microcontroller (such as an Arduino or ESP32). If the values from the sensors differ significantly, it suggests a leak in the pipeline. This real-time comparison enables accurate detection of anomalies in the system. The collected data is also forwarded for logging and monitoring, making this module the core of the system’s leak detection mechanism.
ARDIUNO UNO
POWER SUPPLY
WATER FLOW SENSOR(2)
PIPE SETUP

## Slide 15: Leakage Control and Prevention Module:
Upon detecting a leakage, this module takes immediate action to minimize water wastage. It uses a Solenoid Valve to automatically cut off the water supply, preventing further leakage. Simultaneously, the Pump Motor is turned off via a Relay Module, ensuring that water does not continue flowing. This automated response is managed by the Microcontroller, which receives signals from the sensors and executes the control logic. The system remains inactive until the issue is fixed, making it efficient and safe. This module ensures prompt containment of leaks, reducing damage and maintenance costs.
ARDIUNO UNO
POWER SUPPLY
SOLINOID VALVUE
PIPE SETUP
MOTOR DRIVER
PUMP MOTOR(2)

## Slide 16: Notification and IoT Monitoring Module:
This module focuses on alerting the user and enabling remote access. When leakage is detected, the GSM Module sends an SMS Alert to the user’s phone, providing immediate notification. At the same time, the system updates real-time status on an IoT Webpage using a Wi-Fi Module (e.g., built-in on ESP32). This allows users to monitor water flow data, system status, and leakage history remotely. The module ensures that users stay informed and can take action even when away, enhancing the reliability and usability of the system in smart home and industrial environments.
ARDIUNO UNO
POWER SUPPLY
GSM
ANDROID
IOT

## Slide 17
WORKING PRINCIPLE:
The water leakage detection and control system operates using two water flow sensors, a solenoid valve, a pump motor, a GSM module, and IoT integration. One water flow sensor is installed at the inlet to measure the total water flow entering the system, while the second sensor is placed downstream to monitor the actual flow at the output. If the readings of both sensors do not match, it indicates a leakage in the pipeline. When a leakage is detected, the system immediately triggers the solenoid valve to close the water supply, preventing further wastage. Simultaneously, the pump motor is deactivated to stop the water flow, ensuring minimal loss and damage. The GSM module plays a crucial role in alerting the concerned individual by sending an SMS notification about the leakage incident. Additionally, the system updates the status on an IoT webpage in real-time, allowing remote monitoring and management. This IoT-based feature provides continuous water flow monitoring and logs data for analysis. The project enhances water conservation by preventing leaks from causing excessive wastage and potential structural damage. It also ensures a prompt response to leaks, reducing maintenance costs and increasing the efficiency of the water distribution system. The integration of GSM and IoT makes the system highly reliable, as users can take immediate action upon receiving alerts. The pump motor resumes operation only after the leakage is fixed and system stability is restored. This automated approach ensures a smart and efficient way of detecting and addressing water leaks, making it an ideal solution for residential, industrial, and agricultural water management applications.

## Slide 18: SOFTWARE REQUIREMENTS:
ARDUINO IDE
EMBEDDED C

## Slide 19: APPLICATIONS:
Residential and Commercial Water Management – The system can be used in homes, apartments, offices, and commercial buildings to monitor water usage, detect leaks, and prevent water wastage, ensuring efficient water conservation.
Industrial and Agricultural Applications – In industries and agriculture, the system helps monitor water flow in pipelines and irrigation systems, preventing leaks, optimizing resource utilization, and improving overall water management for sustainable operations.

## Slide 20: ADVANTAGES:
1. Real-Time Monitoring and Automated Alerts – The system continuously monitors water flow and detects leakages instantly. When a leak is identified, an automated buzzer alert is triggered, and real-time data is sent to the cloud via IoT, ensuring immediate action and minimizing water wastage.
2. Enhanced Water Management and Sustainability – By integrating IoT and cloud storage, users can remotely track water consumption, analyze historical data, and optimize water usage. This improves efficiency in residential, industrial, and agricultural applications, contributing to sustainable water conservation.

## Slide 21: FUTURE ENHANCEMENT:
In the future, this system can be enhanced by integrating advanced sensors and machine learning algorithms to predict leakages before they occur based on flow patterns and usage behavior. The addition of a mobile application can provide real-time alerts, usage analytics, and remote control features, improving user convenience. Incorporating a smart valve system can enable automatic shut-off in case of major leaks, preventing water damage. Solar power integration can make the system energy-efficient and suitable for remote areas. Furthermore, extending the system to monitor water quality parameters like pH and turbidity can transform it into a comprehensive smart water management solution.

## Slide 22: CONCLUSION:
In conclusion, the water leakage detection and control system presents a smart, efficient, and automated approach to water management. By utilizing components such as water flow sensors, solenoid valve, pump motor, GSM module, and IoT integration, the system ensures accurate leak detection, immediate response, and real-time monitoring. It not only helps in preventing water wastage and structural damage but also reduces maintenance costs through timely alerts and automated control. The incorporation of GSM and IoT technologies adds value by enabling remote access and instant communication. Overall, this system offers a practical and scalable solution for residential, industrial, and agricultural water management applications, promoting sustainability and resource efficiency.

## Slide 23: REFERENCE:
[1] J. Widagdo, D. D. Putra, B. Syihabuddin, T. Juhana, E. Mulyana, and A. Munir, ‘‘Android-based disaster management application for after-disaster rapid mobile assessment,’’ in Proc. IEEE Int. Conf. Internet Things Intell. Syst. (IoTaIS), Jan. 2021, pp. 201–204, doi: 10.1109/IoTaIS50849.2021.9359695.
[2] T. Yudistira, J. Metaxian, M. Putriastuti, S. Widiyantoro, N. Rawlinson, F. Beauducel, Z. Zulfakriza, A. D. Nugraha, A. Laurin, A. A. Fahmi, and A. Budi-Santoso, ‘‘Imaging of a magma system beneath the Merapi Volcano complex, Indonesia, using ambient seismic noise tomography,’’ Geophys. J. Int., vol. 226, no. 1, pp. 511–523, Mar. 2021, doi: 10.1093/gji/ggab104.
[3] P. Supendi, A. D. Nugraha, S. Widiyantoro, J. D. Pesicek, C. H. Thurber, C. I. Abdullah, D. Daryono, S. H. Wiyono, H. A. Shiddiqi, and S. Rosalia, ‘‘Relocated aftershocks and background seismicity in eastern Indonesia shed light on the 2018 Lombok and Palu earthquake sequences,’’ Geophys. J. Int., vol. 221, no. 1, pp. 1845–1855, Dec. 2019, doi: 10.1093/gji/ggaa118.
[4] F. A. Maulana, Fungsi Koordinasi Badan Penanggulangan Bencana Daerah (BPBD) Sidoarjo Dalam Penanggulangan Bencana Di Kabupaten Sidoarjo. Surabaya, Indonesia: Universitas Pembangunan Nasional ‘Veteran’ Jatim, 2020.
[5] Y. Widyani and H. Laksmiwati, ‘‘Preliminary design of spatio-temporal disaster database in Indonesia to support emergency response,’’ in Proc. Int. Conf. Electr. Eng. Informat. (ICEEI), Aug. 2015, pp. 517–522, doi: 10.1109/ICEEI.2015.7352555.

## Slide 24: REFERENCE:
[6] Badan Nasional Penanggulangan Bencana. (2021). Catatan Refleksi Akhir Tahun Penanggulangan Bencana 2021. 2021 BNPB mencatat 3.092,dan erupsi gunung api 1. diakses pada 1 Juni 2022 Pukul 21:40 WIB. [Online]. Available: https://www.bnpb.go.id/berita/catatan-refleksi-akhirtahun-penanggulangan-bencana-2021#:~:text=Sepanjang
[7] A. H. Tantri and N. A. Rakhmawati, ‘‘Designing a natural disaster ontology for Indonesia,’’ in Proc. 12th Int. Conf. Inf. Commun. Technol. Syst. (ICTS), Jul. 2019, pp. 130–134, doi: 10.1109/ICTS.2019.8850979.
[8] H. Riza, E. W. Santoso, I. G. Tejakusuma, and F. Prawiradisastra, ‘‘Advancing flood disaster mitigation in Indonesia using machine learning methods,’’ in Proc. Int. Conf. ICT Smart Soc. (ICISS), Nov. 2020, pp. 1–4, doi: 10.1109/ICISS50791.2020.9307561.
[9] A. Fariza, N. P. Abhimata, and J. A. N. Hasim, ‘‘Earthquake disaster risk map in east Java, Indonesia, using analytical hierarchy process— Natural break classification,’’ in Proc. Int. Conf. Knowl. Creation Intell. Comput. (KCIC), Nov. 2016, pp. 141–147, doi: 10.1109/KCIC.2016. 7883638.
[10] R. Y. Setiawan, R. D. Susanto, A. Wirasatriya, I. Alifdini, A. D. Puryajati, L. Maslukah, and N. Nurdin, ‘‘Impacts of tropical cyclone Seroja on the phytoplankton chlorophyll—A and sea surface temperature in the Savu Sea, Indonesia,’’ IEEE Access, vol. 9, pp. 152938–152944, 2021, doi: 10.1109/ACCESS.2021.3125605.

## Slide 25: THANK YOU